## Slide 1: Electric Current & Circuits
*slides adapted from Mosley/Bertrand

## Slide 2: Electromotive Force (EMF)
Chemical reactions move electrons from one terminal to the other making one terminal positively charged and the other negatively charged.
This creates an electric potential (V) difference.
A 9V battery means that a 1 C charge that leaves the terminal has 9 J of energy. (9J/1C = 9V)

## Slide 3: Why do charges flow?
The battery creates an electric field within the wire.
The field exerts a force on the charges.
  The charges that are free to move will then move through the electric field.
Flowing charges are called current.

## Slide 4: Current
Current is the amount of charge that passes a given point in a given time.
  Current is the rate of flow of charge
  I : current (ampere, A)
  Q: charge (coulombs, C)
  T: time (seconds, s)

## Slide 5: DC vs. AC
Direct current – the charges always flow in the same direction
Alternating current – the direction of flow changes from moment to moment

## Slide 6: Sample Problem
How many electrons per hour flow past a point in a circuit if it bears 11.4 mA of direct current?

## Slide 7: Conventional Current
We know today that is the electrons that exit the negative terminal of the battery and flow toward the positive terminal.
HOWEVER…
Historically, it was thought that the positive charges flowed from positive to negative. This direction of flow is called conventional current and is what is used.
This is in the direction of higher potential to lower potential.

## Slide 8: Ohm’s Law
Current is directly proportional to voltage and inversely proportional to resistance.
  Greater voltage differences give a greater current
  Greater resistance gives a lower current

## Slide 9: Sample Problem
Determine the current through a 333 Ω resistor if the voltage across the resistor is observed to be 1.5 V.

## Slide 10: Resistance & Resistivity (20.3)
Resistance is directly proportional to length of the material.
  longer wires have higher resistance
Resistance is inversely proportional to cross-sectional area.
  “thicker” wires have lower resistance
The other factor is related to the material itself and is called resistivity.
  Table 20.1 has the resistivity of various materials.

## Slide 11: Resistance
R: resistance (ohms, Ω)
ρ: resistivity (Ω∙m)
L: length (m)
A: cross-sectional area (m2)

## Slide 12: Sample Problem
What is the resistivity of a substance which has a resistance of 1000 Ω if the length of the material is 4.0 cm and its cross sectional area is 0.20 cm2?

## Slide 13: Sample Problem
What is the resistance of a kilometer of copper wire if the diameter is 5.0 mm? (resistivity of copper is 1.72 x 10-8)

## Slide 14: Electric Power
Electric power is calculated by:
Where does this equation come from?
How else can you write this equation?

## Slide 15: Sample Problem
If electrical power is 5.54 cents per kilowatt hour, how much does it cost to run a 100-W light bulb for 24 hours?

## Slide 16: Sample Problem
How much current flows through a 100-W light bulb connected to a 120 V DC power supply?
What is the resistance of the bulb?

## Slide 17: Circuit Wiring

## Slide 18: Sample Problem
If a typical AA cell has an emf of 1.5 V, how much emf do 4 AA cells provide?
Draw the battery composed of these 4 cells.

## Slide 19: Sample Problem
Draw a single loop circuit that contains a cell, a light bulb, and a switch. Name the components.

## Slide 20: Sample Problem
Now put a voltmeter in the circuit so it reads the potential difference across the light bulb.

## Slide 21: Sample Problem
Draw a circuit with a cell and two bulbs in series.

## Slide 22: Sample Problem
Draw a circuit having a cell and four bulbs. Exactly two of the bulbs must be in parallel.

## Slide 23: Mini Lab #1
Draw a circuit containing one cell, one bulb, and a switch. Create this circuit.
Measure the voltage across the cell and across the bulb. What do you observe?

## Slide 24: Mini Lab #2
Draw a circuit containing two cells in series, one bulb, and a switch. Wire this circuit.
What do you observe happens to the bulb?
Measure the voltage across the batteries and across the bulb. What do you observe?

## Slide 25: Mini Lab #3
Draw a circuit containing two cells in series, two bulbs in series, and a switch. Wire this on your circuit board.
What do you observe happens to the bulbs when you unscrew one of them?
Measure the voltage across the battery and across each bulb. What do you observe?

## Slide 26: Mini Lab #4
Draw a circuit containing two cells in series, two bulbs in parallel, and a switch. Wire this on your circuit board.
What do you observe happens to the bulbs when you unscrew one bulb?
Measure the voltage across the battery and across each bulb. What do you observe?

## Slide 27: Sample Problem
Draw a single loop circuit containing two resistors and a cell. Draw voltmeters across each component.

## Slide 28: Sample Problem
Draw a circuit with a AA cell attached to a light bulb of resistance 4 Ω.
Determine the current through the bulb.

## Slide 29: Mini Lab #5
Set up your digital multi-meter to measure resistance. Measure the resistance of the each light bulb on your board. Record the results.
Wire the three bulbs together in series, and draw this arrangement. Measure the resistance of all three bulbs together in the series circuit. How does this compare to the resistance of the individual bulbs?
Wire the three bulbs together in parallel, and draw this arrangement. Measure the resistance of the parallel arrangement. How does this compare to the resistance of the individual bulbs?

## Slide 30: Series Wiring
Current is the same in each device.
If current in one component is interrupted, current is interrupted in the other components.
Voltage is divided between the resistors.
Equivalent resistance is given by:

## Slide 31: Sample Problem
What is the equivalent resistance of a 100 Ω, a 330 Ω and a 560 Ω resistor when these are in a series arrangement?

## Slide 32: Parallel Wiring
Voltage drop is the same across each branch.
If current in one branch is interrupted, current continues to flow through the others.
Equivalent resistance is given by:

## Slide 33: Kirchoff’s Rules
Junction rule – the total current directed into a junction must equal the total current directed out of the junction.
Loop rule – around a closed circuit loop, the total of all the potential rises must equal the total of all the potential drops. (COE)

## Slide 34: Kirchoff’s Rules
Junction rule – the total current directed into a junction must equal the total current directed out of the junction.
Loop rule – around a closed circuit loop, the total of all the potential rises must equal the total of all the potential drops. (COE)

## Slide 35: Kirchoff’s Rules
Junction rule – the total current directed into a junction must equal the total current directed out of the junction.
Loop rule – around a closed circuit loop, the total of all the potential rises must equal the total of all the potential drops. (COE)

## Slide 36: Sample Problem
Find the current I4 (magnitude and direction).

## Slide 37: Sample Problem
Use the loop rule to determine the potential drop across the light bulb.
V
V
1.5 V
9 V
2 V
3 V

## Slide 38: Measuring Current & Voltage
When measuring current:
  the ammeter must be part of the circuit
  an ideal ammeter should have small resistance
When measuring voltage:
  the voltmeter should be connected between the two points
  an ideal voltmeter should have infinite resistance

## Slide 39: Terminal Voltage and EMF
When a current is drawn from a battery, the voltage across its terminals drops below its rated EMF.
The chemical reactions in the battery cannot supply charge fast enough to maintain the full EMF.
Thus the battery is said to have an internal resistance, designated r.
Ex: Starting a car with the headlights on, the lights dim. The starter draws a large current and the battery voltage drops as a result.

## Slide 40: Terminal Voltage and EMF
A real battery is then modeled as if it were a perfect emf Ɛ. in series with a resistor r.
Terminal voltage Vab
When no current is drawn from the battery, the terminal voltage equals the emf.
When a current I flows from the battery, there is an internal drop in voltage equal to Ir, thus the terminal voltage (actual voltage delivered) is Vab = Ɛ - Ir

## Slide 41: Sample Problem
A car battery has an emf of 12.0 V and an internal resistance of 0.010 Ω. What is the terminal voltage when the current drawn from the battery is 10.0 A? 100.0 A?

## Slide 42: Series Circuit
Resistors “in a row”
Only one path for current to flow
If one resistor (bulb) in a series circuit goes out, they all go out – break in the circuit
Total Resistance for resistors in a series:
R2
R1
R3

## Slide 43: Series Circuit
Kirchhoff’s Loop Rule
  Sum of voltage in a closed loop is equal to zero
  Voltage between two points in a circuit is the same, regardless of the path taken!
  Remember:

## Slide 44: Ex: Series Circuit Analysis
3Ω
Vab = 12V
Vcb = _____
Vdc = _____
Vad = _____
I1 = _____
RT = _____
1Ω
12V
2Ω
b
c
d
a

## Slide 45: Parallel Circuits
More than one path for the current
Have ‘parallel paths’ in the circuit
If one resistor (bulb) in a parallel circuit goes out, the other branches stay lit
a
3Ω
12V
b
I1
12Ω
I2
I3

## Slide 46: Parallel Circuits
Total resistance in a parallel circuit:
These mean the same thing, but the bottom one is easier to plug in and calculate!

## Slide 47: Parallel Circuits
  RECALL: Kirchhoff’s Loop Rule:
   The sum of the voltage around a closed loop = zero.
   The voltage between any two points on a circuit will be the same regardless of the path taken
  Kirchhoff’s Junction Rule – (“A Herd of Chickens”)
   The sum of the current entering a junction is equal to the sum of the current leaving the junction
   I1 = I2 + I3 +…

## Slide 48: Parallel Circuits – Junction Rule
a
b

## Slide 49: Ex: Parallel Circuit Analysis
Vab = 12V
I1 = _____
I2= _____
I3= _____
RT = _____
a
3Ω
12V
b
I1
12Ω
I2
I3

## Slide 50: Complex (Series & Parallel) Wiring
Simplify the circuit by finding equivalent resistances.

## Slide 51: Mini Lab #6
Draw and build an arrangement of resistance that uses both parallel and series arrangements for 5 or 6 resistors in your kit. Calculate and then measure the equivalent resistance. Compare the values.

## Slide 52: Sample Problem
Draw a circuit containing, in order, (1) a 1.5 V cell, (2) a 100- Ω resistor, (3) a 330 Ω resistor in parallel with a 100 Ω resistor (4) a 560 Ω resistor, and (5) a switch.
Calculate the equivalent resistance.
Calculate the current through the cell.
Calculate the current through the 330 Ω resistor.

## Slide 53: CapaciTors in Series & Parallel

## Slide 54: Capacitors in Series & Parallel
For capacitors:
  q = CV
  E = (1/2)CV2

## Slide 55: Capacitors in Series & Parallel
Remember,
  q = CV
  E = (1/2)CV2
Equivalent capacitance in parallel is given by

## Slide 56: Capacitors in Parallel
Equivalent capacitance in parallel is given by

## Slide 57: Capacitors in Series
All capacitors in series, regardless of their capacitances, store the same charge.
Why?!
Equivalent capacitance in series is given by

## Slide 58: Capacitors in Series
Equivalent capacitance in series is given by
Capacitors in series all store the same charge!
Capacitors in parallel have the same voltage (KLR)!

## Slide 59: RC Circuits (20.13)
An RC circuit is a circuit with at least one resistor and at least one capacitor.
When current is allowed to flow, charge builds on the plates until q=CV0 (V0 is the battery voltage)

## Slide 60: Charging a Capacitor
q = charge (C)
q0 = equilibrium charge (C)
e = 2.718…
t = time (s)
RC = τ = time constant (s)

## Slide 61: Charging a Capacitor
Sketch a graph of charge vs. time for the process of charging a capacitor.

## Slide 62: Discharging a Capacitor
Sketch a graph of charge vs. time for the process of discharging a capacitor.

## Slide 63: Discharging a Capacitor
Small values of the time constant lead to a rapid discharge

## Slide 64: Sample Problem
The circuit in the drawing contains two resistors and two capacitors that are connected to a battery via a switch. When the switch is closed, the capacitors begin to charge up. What is the time constant for the charging process? What is the charge on the capacitor after 0.005 s?

## Slide 65: RC Circuits
An RC circuit is a circuit with at least one resistor and at least one capacitor.
When current is allowed to flow, charge builds on the plates until q=CV0 (V0 is the battery voltage)